| CONTROL TROUBLESHOOTING CHART WIRE PENDANT |
| --- |
| No functions working | Not receiving power | Check crane control socket Pin E ensure that it is receiving 12V |
|  |  | With the plug disconnected, activate a function switch then check continuity between Pin E and the activated function/direction pin |
|  |  | For example: activate Hoist Down and check for continuity between Pin E and Pin P |
| One function not working | Faulty wiring/switch malfunction | With the plug disconnected, activate the function that is not working and check for continuity between Pin E and corresponding function pin |
| All functions slow | Trigger problem | Check Crane Control Module for Error Code 5 and Proportional Output |
| (APPLIES TO PROPORTIONAL CRANES ONLY) |  |  |
|  | Valve driver problem | Calibrate valve driver board |

# Text boxes

Figure 1 CONTROL PLUG ON PENDANT

Figure 2 CRANE CONTROL MODULE